## Slide 1: Hardware Programming HWP01
capturing a
FPGA
design with
VHDL

## Slide 2: Planning: theory
First week
  Introduction digital systems
  Introduction to FPGAs
  Structured digital Design
  Modeling concepts in VHDL
Second Week
  Introduction VHDL
  Code structure
  Data types
Third week
  Combinational versus sequential design
  Concurrent and sequential code
  Signals and variables
Fourth week
  Introduction to state machines
Fifth week
  Designing state machines
  Advanced VHDL design

## Slide 3: Agenda
Discussion of previous week
Introduction to VHDL
Design verification
Code structure and data types
Notes: Wat weten we nog van vorige week?
FGPA is gewoon heel snel en kan potentieel alles.
VHDL: Alles gebeurt op hetzelfde moment
  Het is dus geen code die uitgevoerd wordt, maar een schakeling die gewoon “is”
Wat is onze aanpak als we iets op de FPGA willen zetten?
  Architectuur
  Realiseren/Simuleren
  Testen
Beschrijven van een functie
  Behavioral
  Structural

## Slide 4: Agenda
Discussion of previous week
Introduction to VHDL
Design verification
Code structure and data types

## Slide 5: Introduction to VHDL
VHSIC was a 1980s U.S. government program to develop very-high-speed integrated circuits. The United States Department of Defense launched the VHSIC project in 1980 as a joint tri-service project. The project led to advances in integrated circuit materials, lithography, packaging, testing, and algorithms, and created numerous computer-aided design tools. A well-known part of the project's contribution is VHDL, a hardware description language.
Standard defined by IEEE in 1987, revisions in 2008 and 2019
Remember: VHDL is not a normal programming language. It describes digital hardware.
Everything happens all the time

## Slide 6: Entity and architecture keywords
ENTITY
  Define a function block and specify the interface to the outside world with PORTS
ARCHITECTURE
  Define the implementation of your entity. Either behavioral or structural

## Slide 7: VHDL Design
Figure adapted from FPGAcenter.com

## Slide 8: Agenda
Discussion of previous week
Introduction to VHDL
Design verification
Code structure and data types

## Slide 9: Design verification: test bench
Functional verification of your design
In this course you will have to create a test bench for every assignment you hand in
Figure adapted from Pedroni.
Notes: Beter plaatje zoeken?

## Slide 10: Test bench overview
A test bench entity has no ports
In the architecture you create port maps to instantiate your design
Generate a clock signal as stimulus
In this course we only cover functional verification; no timing verification

## Slide 11: Delay models
Inertial delay:
  Models delays in gates with the after clause: a <= b AFTER 1 ns;
Transport delay:
  Models delays in wires
Delta delay:
  Delay added automatically by the simulator if no delay is explicitly prescribed
Remember: delay statements are not synthesizable

## Slide 12: Discussion of testbench example
LIBRARY ieee;
USE ieee.std_logic_1164.all;
USE ieee.numeric_std.all;
ENTITY assignment2_tb IS
END ENTITY;
ARCHITECTURE testbench OF assignment2_tb IS
COMPONENT assignment2 IS
PORT (
SW : IN STD_ULOGIC_VECTOR(17 DOWNTO 0);
HEX0 : IN STD_ULOGIC_VECTOR(6 DOWNTO 0);
LEDR : IN STD_ULOGIC_VECTOR(17 DOWNTO 0)
);
END COMPONENT;
SIGNAL SW_tb : STD_ULOGIC_VECTOR(17 DOWNTO 0);
SIGNAL HEX0_tb : STD_ULOGIC_VECTOR(6 DOWNTO 0);
SIGNAL LEDR_tb : STD_ULOGIC_VECTOR(17 DOWNTO 0);
BEGIN
TB: assignment2 PORT MAP (SW => SW_tb, HEX0 => HEX0_tb, LEDR => LEDR_tb);
PROCESS
BEGIN
SW_tb <= "000000000000000000";
FOR I IN 0 TO 15 LOOP
WAIT FOR 10 ns;
SW_tb <= STD_ULOGIC_VECTOR(UNSIGNED(SW_tb) + 1);
END LOOP;
REPORT "Test completed.";
WAIT;
END PROCESS;
END ARCHITECTURE;

## Slide 13
process
type int_array is array(0 to 15) of integer;
constant expexted_seven_segment_code: int_array := (
16#40#, 16#79#, 16#24#, 16#30#,
16#19#, 16#12#, 16#02#, 16#78#,
16#00#, 16#10#, 16#08#, 16#03#,
16#46#, 16#21#, 16#06#, 16#0E#
);
begin
    report "Testing entity assignment2.";
-- Initialize signals.
        sw_tb <= "0000";
      blank_tb <= '1’;
        wait for 10 ns;
        -- Check blank.
        assert hex0_tb = "1111111"
        report "test failed for blank = 1" severity error;
        blank_tb <= '0’;
        -- Loop through all possible values of switches.
        for i in 0 to 15 loop
        sw_tb <= std_ulogic_vector(to_unsigned(i, sw_tb'length));
        wait for 10 ns;
        -- Check result.
        assert hex0_tb = std_ulogic_vector(to_unsigned(
        expexted_seven_segment_code(i), hex0_tb'length
        ))
        report "test failed for i = " & to_string(i)
        severity error;
        end loop;
        report "Test completed.";
        std.env.stop;
    end process;
end architecture;

## Slide 14: Agenda
Discussion of previous week
Introduction to VHDL
Design verification
Code structure and data types

## Slide 15: Logic values
See book chapter 7.6.2
There are 4 synthesizable logic values
  ‘0’, ‘1’, ‘-’ and ‘Z’.
There are 5 other useful logic values
  ‘L’ = (‘0’), ‘H’ = (‘1’), ‘X’ = (‘-’), ‘W’, ‘U’.
You should not use any other then the 4 synthesizable logic values

## Slide 16: Resolved and Unresolved
Multiple drivers are driving a logic signal
  Is this correct?
  What happens?
Unresolved
Resolved
Detailed explanation

## Slide 17: Example: AND gate
---------------------------------------------
LIBRARY ieee;
USE ieee.std_logic_1164.all;
---------------------------------------------
ENTITY andgate IS
PORT (a,b: IN STD_ULOGIC;
c: OUT STD_ULOGIC);
END andgate;
---------------------------------------------
ARCHITECTURE voorbeeld OF andgate IS
BEGIN
c <= A AND B;
END voorbeeld;
---------------------------------------------
Notes: std_ulogic heeft de voorkeur. Ik vind dat geschreeuw in hoofdletters ook niet mooi, maar dat kan later wel eens aangepast worden.

## Slide 18: Libraries
---------------------------------------------
LIBRARY library_name;
USE library_name.package_name.all;
---------------------------------------------
The most frequently used packages are:
Package standard, from the library std (visible by default)
Library work (where the projects are saved is visible by default)
Package std_logic_1164, from the library ieee (when needed, must be explicitly declared)
---------------------------------------------
LIBRARY std; -- optional declaration
USE std.standard.all; --optional
LIBRARY work -- optional
USE work.all -- optional; also not needed if defined as below
USE work.my_package.all; --if an extra user made package is needed
LIBRARY ieee;
USE ieee.std_logic_1164.all
---------------------------------------------

## Slide 19: INCLUDE : IEEE.STD_LOGIC_1164 LIBRARY
---------------------------------------------
LIBRARY ieee;
USE ieee.std_logic_1164.all;
---------------------------------------------
https://www.csee.umbc.edu/portal/help/VHDL/std_logic_1164.vhdl
Defines STD_LOGIC as well as STD_LOGIC_VECTOR (array of STD_LOGIC)
'U', -- Uninitialized
'X', -- Unknown
'0', -- LOGIC 0
'1', -- LOGIC 1
'Z', -- High Impedance (used for tri-state I/O’s)
'W',-- Weak signal
'L', -- Weak signal with logic 0 as preference
'H', -- Weak signal with logic 1 as preference
'-' -- Don't care
Simulation or Synthesis?
Defines various FUNCTIONS, such as EDGE DETECTION
-------------------------------------------------------------------
FUNCTION rising_edge (SIGNAL s : std_ulogic) RETURN BOOLEAN;
FUNCTION falling_edge (SIGNAL s : std_ulogic) RETURN BOOLEAN;

## Slide 20: Data Types: IEEE 1164 Standard Logic
IEEE’s std_logic_1164 examples:
STD_ULOGIC
STD_ULOGIC_VECTOR
SIGNAL b: STD_ULOGIC_VECTOR (7 DOWNTO 0);
b <= “1100ZZZZ”; -- array of 8 std_logic’s
-- in MSB representation
SIGNAL a: STD_ULOGIC;
a <= ‘0’; -- a is zero
a <= ‘1’; -- a is one
a <= ‘Z’; -- a is high-impedance
-- used for bidi ports

## Slide 21: Data Types: IEEE.numeric_std.all LIBRARY
  Allows for: unsigned, signed, integer, natural
  Contains many functions such as: abs(), + addition, - subtraction, * multiplication, / division, etc…, that can be used with these types
  As well as: >, <, <=, >=, =, sll, srl
  Normal STD_LOGIC_VECTORS: can’t calculate with those!
  Additional Type conversion functions needed to overcome this…..
  Zie H10.7 van het boek.
---------------------------------------------
LIBRARY ieee;
USE ieee.numeric_std.all;
---------------------------------------------
https://www.csee.umbc.edu/portal/help/VHDL/numeric_std.vhdl
Notes: Op het bord:
3 typen opschrijven. Logic, (un)signed, integer
Hoe zien deze er uit
Verschillende bespreken
Waar gebruik je elk type voor?

## Slide 22: Conversion of Common Types
SIGNAL a: STD_LOGIC_VECTOR(7 DOWNTO 0);
SIGNAL b: UNSIGNED (7 DOWNTO 0);
SIGNAL c: SIGNED (7 DOWNTO 0);
(un)signed → std_logic_vector
std_logic_vector → (un)signed
a <= STD_LOGIC_VECTOR(b);
a <= STD_LOGIC_VECTOR(c);
b <= UNSIGNED(a);
c <= SIGNED(a);

## Slide 23: Conversion of Common Types
SIGNAL d: UNSIGNED (7 DOWNTO 0);
SIGNAL e: SIGNED (7 DOWNTO 0);
SIGNAL f: INTEGER RANGE 0 TO 255;
SIGNAL g: INTEGER RANGE -128 TO 127;
integer → (un)signed
(un)signed → integer
d <= TO_UNSIGNED(f, 8); -- d is an array of 8
e <= TO_SIGNED(g, 8); -- e is an array of 8
f <= TO_INTEGER(d);
g <= TO_INTEGER(e);

## Slide 24: Conversion of Common Types
integer → std_logic_vector
SIGNAL h: STD_LOGIC_VECTOR (7 DOWNTO 0);
SIGNAL i: INTEGER RANGE 0 TO 255;
SIGNAL j: INTEGER RANGE -128 TO 127;
std_logic_vector → integer
h <= STD_LOGIC_VECTOR(TO_UNSIGNED(i,i'length);
h <= STD_LOGIC_VECTOR(TO_SIGNED(j,j'length);
i <= TO_INTEGER(UNSIGNED(h));
j <= TO_INTEGER(SIGNED(h));

## Slide 25: Warning
Don’t use it, no matter what older books or websites/forums/code snippets online say!
Use IEEE 1164
ieee.numeric_std.all
instead for unsigned and signed types!
STD_LOGIC_ARITH
is
OBSOLETE

## Slide 26: Assignment Operators
<= for a signal
:= for a variable (covered later)
=> for individual elements of a vector
Example:
signal a: std_logic;
variable b: integer range 0 to 255;
signal c: std_logic_vector(3 downto 0);
a <= '1'; -- assign single bits with '
b := 10; -- assign an integer
c <= "1100"; -- assign a vector with "
c <= (3 => '1', 2 => '1', OTHERS => '0'); –- same as previous line
a <= c(0);

## Slide 27: Other Functions available with numeric_std
Logical
  not, and, or, nand, nor, xor, xnor
Arithmetic
  +, -, *, /, **, mod, rem, abs
    NOTE: Not all synthesizable
Comparison
  =, /=, <, >, <=, >=
Shift operators:
  sll, srl -- shift left logical, shift right logical
  sla, sra -- shift right arithmetic, shift right arithmetic
  rol, ror -- rotate left, rotate right

## Slide 28: Attributes
SIGNAL d : STD_LOGIC_VECTOR (7 DOWNTO 0);
d'LOW = 0 -- laagste array index
d'HIGH = 7 -- hoogste array index
d'LEFT = 7 -- meest linkse array index
d'RIGHT = 0 -- meest rechtse array index
d'LENGTH = 8 -- lengte van de vector
d'RANGE = (7 DOWNTO 0) -- range of the vector
d'REVERSE_RANGE = (0 TO 7) -- reverse range of the vector
Zie H9 van het boek

## Slide 29: Simple Signal Assignment statement
When the Right Hand Side (RHS) of a signal assignment changes, the signal assignment statement is executed
Signals in a circuit are modeled as signal statement assignments in VHDL
Order in text is not preserved!
Notes: Draw a schematic and ask if the the order of signal assignment statements are important

## Slide 30: D flip-flop
We’ll show you a behavioral and structural description of a simple D flip-flop
Figures adapted from Embedded Systems Design: A Unified Hardware/Software Introduction

## Slide 31: Example: DFF (good)
Use rising_edge() function (or falling_edge())
-------------------------------------
LIBRARY ieee;
USE ieee.std_logic_1164.all;
-------------------------------------
ENTITY dff IS
PORT(d, clk, rst: IN STD_LOGIC;
q, qi: OUT STD_LOGIC)
END dff;
-------------------------------------
ARCHITECTURE dff_arch OF dff IS
BEGIN
PROCESS (rst, clk)
BEGIN
IF (rst=‘1’) THEN
q <= ‘0’;
ELSIF rising_edge(clk)
THEN
q <= d;
END IF;
END PROCESS;
qi <= NOT(q);
END dff_arch;

## Slide 32: Example: D-FlipFlop (bad)
In many code snippets people use ‘EVENT like this:
-------------------------------------
LIBRARY ieee;
USE ieee.std_logic_1164.all;
-------------------------------------
ENTITY dff IS
PORT (d, clk, rst: IN STD_LOGIC;
q, qi : OUT STD_LOGIC);
END dff;
-------------------------------------
ARCHITECTURE implementation OF dff IS
BEGIN
PROCESS (rst, clk)
BEGIN
IF (rst=‘1’) THEN
q <= ‘0’;
ELSIF (clk’EVENT AND clk=‘1’) THEN
q <= d;
END IF
END PROCESS;
qi <= NOT(q);
END implementation;
Why is this not a proper DFF?
Hint: think of the values a STD_LOGIC signal can obtain by definition…
Notes: clk kan ook een andere waarde dan ‘0’ en ‘1’ hebben.

## Slide 33: Summary
Introductie in VHDL
Verify the functional behavior of your design with test benches
Use standard functions for conversion of data types

## Slide 34: Homework
Covered today:
  Discussion of previous week
  Introduction to VHDL
  Code structure and data types
  Design verification
Homework:
  2.1, 2.2a, 3.1, 3.20, 3.22, 3.24
Next week:
  Combinational versus sequential design
  Concurrent and sequential code
  Signals versus variables